## Slide 1: Rx Power (Pathloss) Computation
The received samples undergo
  Pre-filtering via a FIR (Remez) LPF
  Initial truncation (dropping the first few samples)
  Time-windowing (choosing samples at either side of the mid-point (w_sz / 2)
  ‘TallEnoughAbs’ Noise Elimination
  FFT  Absolute Values  Squared  Normalized (with n_samples)
  Trapezoidal Numerical Integration over frequency

## Slide 2: Spatial Autocorrelation Coefficient (v Tx-Rx distance)
The received samples undergo:
  Pre-filtering via a FIR (Remez) LPF
  Initial truncation (dropping the first few samples)
  Time-windowing (choosing samples at either side of the mid-point (w_sz / 2)
  ‘TallEnoughAbs’ Noise Elimination
Keeping alignment constant, for a particular Tx-Rx distance value (‘d’)
    There is a reference Rx measurement location corresponding to distance 0
    There is another Rx location corresponding to a Tx-Rx distance of ‘d’
  For both these locations:
    FFT  Absolute Values  Normalized (with n_samples)
    Find sample mean across frequencies
    Expectation with respect to ensemble (all collected measurement samples at the location)

## Slide 3: Items: Plots for IEEE TAP Journal Paper
Power-Delay-Angular-Profiles (PDAPs): AoA vs Delay heatmap [Done – 3 routes (usf)]
Power-Delay-Doppler-Profiles (PDDPs): [Done – 3 routes (usf)]
  Delay vs Doppler Frequency heatmap
  Normalized Power vs Doppler Frequency plot
Pathloss Analyses: [Done – 6 routes (usf, garage, canyon, stadium)]
  Empirical Pathloss for 3 different routes (urban-campus, urban-vegetation, suburban-neighborhood)
  Compare with 3GPP TR38.901 and ITU-R M.2135 UMa standards (urban)
  Compare with METIS and mmMAGIC UMi standards (suburban & vegetation)
Spatial Consistency Evaluations: [Done – 6 routes (usf, garage, canyon, stadium)]
  Spatial Autocorrelation Coefficient vs Tx-Rx Separation vs Excess Delay 3D plot
  Angular Autocorrelation Coefficient vs Tx-Rx Alignment Accuracy vs Excess Delay 3D plot
  Spatial Autocorrelation Coefficient vs Tx-Rx Relative Velocity vs Excess Delay 3D plot
RMS Delay- and Direction-Spread CDFs (Empirical, SV Model, QDC Model) – [Done - 3 routes (usf)]
Dynamic Blockage by pedestrians & parked vehicles: PL vs Time – [Done - 2 routes (garage, canyon)]
Normal Distribution Fitting to Shadow Fading SD from measurements – [Done - 3 routes (usf)]

## Slide 4: Comments
  Cluster inter-arrival times CDFs:
    Poisson arrivals, Exponential inter-arrival times
    MLE on measurements with arrival rate parameter (EM)
    Compare with SV, QDC, and stochastic channel models
    Kolmogorov-Smirnov to determine goodness of CDF fits
  Cluster peak-power v Delay plots:
    Simple linear regression curve-fitting
    Compare with SV, QDC, and stochastic channel models
  RMS delay- and direction-spread CDFs:
    Compare with SV, QDC, and stochastic channel models
    Kolmogorov-Smirnov to determine goodness of CDF fits
  Average fade-depth and fade-duration for fast-fading due to dynamic blockages
    Compare with D2D models from NIST