## Slide 1: A Robotic Antenna Alignment and Tracking System for Millimeter Wave Propagation Modeling
Bharath Keshavamurthy*, Yaguang Zhang^, Christopher R. Anderson#,
Nicolò Michelusi*, James V. Krogmeier^, and David J. Love^
*Electrical, Computer and Energy Engineering, Arizona State University, Tempe, AZ
^Electrical and Computer Engineering, Purdue University, West Lafayette, IN
#Electrical Engineering, United State Naval Academy, Annapolis, MD

## Slide 2: Motivation
Widespread 5G deployments using the mid-band spectrum
Operators have now shifted focus on to the mmWave spectrum
  Enhancement in UX vis-à-vis data rates & latencies
  Propagation challenges
Academic research has also gained a renewed emphasis
June 20, 2019
Nov 14, 2018

## Slide 3: Features & Contributions: System Design
A fully autonomous V2X* mechanical beam-steering platform[1]
Cost- & computationally-effective vs electronic beam-alignment strategies[2]
The principal axes positioning accuracy = 1.1o
The beam-steering response time = 27.8 ms
3-D geo-positioning accuracy of 17 cm with real-time kinematics
Real-time route visualizations via Plotly-Dash/MapBox
Real-time sample visualizations & efficient data storage (with redundancy)
* Can be easily scaled to V2V settings
[1] M. Comiter et al., “Millimeter-wave field experiments with many antenna configurations for indoor multipath environments,” in 2017 IEEE Globecom Workshops (GC Wkshps), 2017, pp. 1–6.
[2] H. Hassanieh et al., “Fast millimeter wave beam alignment,” in 2018 ACM Special Interest Group on Data Communication (SIGCOMM), p. 432–445, doi: 10.1145/3230543.3230581.

## Slide 4: Features & Contributions: Measurement Campaign
28 GHz sliding-correlator channel sounder[3]
NSF POWDER testbed at the University of Utah in Salt Lake City, UT
  BYOD flexibility
  FCC experimental license to utilize the 27 – 29 GHz spectrum
  Dell PowerEdge R740 compute nodes (x4) provisioned from Emulab computing cluster
Tx mounted on the roof-top of the William Browning Building
Rx mounted on a van/cart and driven/pushed around campus
Geographically diverse site: Both urban and suburban environments[4]
[4]: Y. Zhang et al., “28-GHz channel measurements and modeling for suburban environments,” in 2018 IEEE Intl. Conf. Commun., 2018, pp.1–6
[3]: R. J. Pirkl and G. D. Durgin, “Optimal sliding correlator channel sounder design,” IEEE Trans. Wireless Commun., vol. 7, no. 9, pp. 3488–3497, 2008.

## Slide 5: The Sliding-Correlator Channel Sounder

## Slide 6: Tx Design

## Slide 7: Rx Design

## Slide 8: Operational Parameters
Parameter Name | Parameter Value (on-site)
Carrier Frequency | 28 GHz
Chip Sequence Length | 2047
RF Bandwidth | 800 MHz
Tx Chip Rate | 400 Mcps
Temporal Resolution | 2.5 ns
Rx Chip Rate | 399.95 Mcps
Tx/Rx Antenna Gain | 23 dBm
Measured Tx/Rx Azimuth HPBW | 10.1o
Measured Tx/Rx Elevation HPBW | 11.5o
Maximum Measurable Path Loss | 182 dB

## Slide 9: Rx GNURadio Sink Parameters
A Raspberry-Pi host coupled with a USRP B200mini (TX/RX Channel)
Bandwidth = 0 Hz
Gain = 0 dB and 76 dB
Center Frequency = 2.5 GHz
Sample Rate = 2 Msps
QT GUI Time Sink: Dynamic limits & triggers for real-time visualizations over WLAN

## Slide 10
The signal observed at the input of the 28 GHz up-converter in the Tx circuit
The power-delay profiles observed in the Rx circuit (2.5 GHz swept at 10 ms)

## Slide 11: The Autonomous Beam-Steering System

## Slide 12: PT2645-S: Schematics
ServoCity PT2645-S Pan & Tilt Kit: Design Schematic
ServoCity HSR-2645CRH Servo: Design Schematic

## Slide 13: PT2645-S: Design Parameters
Open-loop pan & tilt platform
Yaw and Pitch axes driven by an HSR-2645CRH continuous rotation servo
Gear ratio (both axes) is 7:1
  12 teeth on the servo gear
  84 teeth on the mount gear
5 lbs maximum payload

## Slide 14: HSR-2645CRH Servo: Specifications
Parameter Name | Parameter Value
Output Shaft Style | C24T-Spline
Voltage Range | 4.8 – 7.4 V
No-Load Speed (4.8 V) | 46 rpm
Stall Torque (4.8 V) | 111.09 oz-in (8 kg-cm)
Pulse Amplitude | 3 – 5 V
Direction with Increasing PWM Signal | Clockwise
Feedback Style | No positional feedback (open-loop continuous rotation servo)
Output Shaft Support | Dual Ball Bearings
Weight | 1.87 oz (53 g)
Motor Type | Carbon Brushed Cored Motor

## Slide 15
Rotational Platform Testing: Laser Testbed | Image Recognition
Rotational Platform + Communication System: Laboratory Testing Setup

## Slide 16
GPS Translation: UBlox GPS messages (with RTCM3.0 corrections) over I2C  Internal NMEA format over Serial  JSON events streamed over Kafka

## Slide 17
JSON GPS Event Sample
(streamed over Kafka for Tx/Rx alignment)
IMU Event Sample
(logged internally for post-processing)

## Slide 18: The Complete System Architecture

## Slide 19: Pre-Deployment Calibration

## Slide 20
Pre-Deployment Calibration Setup: Tx
Pre-Deployment Calibration Setup: Variable Attenuator + Rx

## Slide 22: On-Site Deployment

## Slide 23
Tx Installation and Testing: Rooftop mount | Weather-proofing | Signal tests on a handheld spectrum analyzer

## Slide 24
Rx Deployment and Data Collection: Installation on a cart (urban-vegetation) | Real-time visualization of power-delay-profile samples

## Slide 25: Platform Features & Results

## Slide 26
Real-time Orchestration: Tx monitoring & troubleshooting via an Android Debug Bridge | Rx route visualizations
Rx route visualized in Plotly-Dash/MapBox as it is being traversed
Fixed Tx location

## Slide 27
Geo-positioning Accuracy on-site: 2-D accuracy of 9 cm & 3-D accuracy of 17 cm – with RTCM3.0 and 28 satellites-in-view

## Slide 28
Antenna Pattern: Azimuth
Antenna Pattern: Elevation

## Slide 29
Post-Processing: Received signal power values superimposed on a Google Hybrid map of the site under analysis – President’s Circle (urban)

## Slide 30
Post-Processing: Received signal power values superimposed on a Google Hybrid map of the sites under analysis –
Campus Vegetation/Foliage (urban) and Campus Fraternities (suburban)

## Slide 31: Thank you

## Slide 32: Q & A